## Slide 1: CSCE 430 Project $$Cache Money$$
Brett Baumert
Curtis Johnson
Jake Reisdorff`

## Slide 2: Overview - Our design process
Came up with overall design (instructions, etc)
Developed Assembler
Constructed datapath
  Construction of individual stages
  Connection of each stage
  Implementation of other components

## Slide 3: Overall Design
Based on MIPS 5 stage pipeline design
32 bit instruction length
Nine total instructions
  Add, Add Immediate, Multiply, Load Word, Store Word, Branch on Equal, Branch on Not Equal, Jump, and No Operation (nop)
  Subset of MIPS tailored for our usage

## Slide 4: Assembler
Written in Java!
Is not responsible for optimaztion

## Slide 5: Assembler
Assembler carries much abstraction
Each Instruction implements one or several interfaces, depending upon its usage (Arithmetic, Immediate, etc)
Adaptability
  To add a new instruction, determine its type, and implement the required interfaces (Very easy)
  Adapt datapath for the new instruction

## Slide 6: Datapath Design
Accounted for multiple types of hazards
Developed each stage individually
Integrated required stages / components
Testing / Future Work

## Slide 7: Branch Prediction
Implemented as always ‘not taken’
Branching Logic contained within the control unit in the ID (Instruction Decode) stage
Penalty? One cycle!

## Slide 8: Handling Hazards
Hazard Detection Unit
  All hazards resolved in hardware
Control Unit
  Handles flushing of stages
  Handles stalling of pipeline

## Slide 9: Branch Hazards
add $2, $3, $0
beq $2, $5, somewhere
Introduces a RAW (Read after Write) hazard
Did not want to extend forwarding logic to ID stage
Solution: Insert bubbles!

## Slide 10: Load Word Stall
lw $31, $13
add $2, $31, $31
Can’t depend on forwarding values from memory
High latency
Solution: Insert bubble!

## Slide 11: Other Data Hazards
add $2, $3, $1
add $4, $2, $2 Data Dependencies
Ensure each instruction has the most up-to-date value
Solution: Fowarding Unit for multiple stages

## Slide 12: Forwarding Unit
Interconnects multiple stages, including Execution Stage, Memory Stage, and Register Write Back Stage
Forwards most up to date values to the Execution Stage where they are needed
Handles prioritization (Value from Memory Stage should take precedence over Write Back Stage)

## Slide 13: Memory Implementation
Use of Quartus megafunction RAM blocks
  Why?
Directly loaded file from assembler output
Existed in both Instruction Fetch Stage and Memory Stage
Essentially, these act as caches for our pipeline

## Slide 14: Other Useful Tidbits
Processor clock: 50 MHz
Both Memory Blocks (Data caches) hold 1 KB of data
  The 10x10 matrix case used ~97% of memory block
Entire implementation : ~9% of FPGA
Performed matrix multiplication!
17 Warnings! (No inferred latches…)

## Slide 15: Significance of Pipeline
Overall Faster Processor
  Ability to greatly increase the clock speed!
Hardware Abstraction
  Like software abstraction, creates modules that work together, but are mostly independent of one another.

## Slide 16: Problems Encountered
Accounting for many hazards throughout the pipeline
  Debug time
  Compile time…
Inferred Latches (VHDL)
SRAM/Cache Integration
  Interfacing with the SRAM
  Using multiple cycles to read from memory into cache / write through to cache / satisfy requests from both IF and Memory stages
  Needed a cache & memory controller…

## Slide 17: Money Machine
Money Machine – a completely on-chip cache and memory controller, usable throughout the entire pipeline.

## Slide 18: Money Machine

## Slide 19: Teamwork
Much collaboration took place in designing everything from instruction set to working processor
Each member was involved in every aspect of the project

## Slide 20: end: jmp end